Data set IIIb: Non-stationary 2-class BCI data
Group information:
Center of Neuroinformatics
School of Life Science and Technology
University of Electronic Science and Technology of China (UESTC)
Chengdu, 610054, P. R. China
Supervisor: Dezhong yao  E-mail: dyao@uestc.edu.cn
Team Member: Yu Yin ,Xiang Liao

Description of our analysis method




 







Processing Procedure: 
Select subject-specified scales of the complex Morlet wavelet by a statistical method;
Transform the EEG data s(t) with the complex Morlet wavelet on the selected scale, and calculate the squared wavelet coefficient as the element of the following feature vector.
 , is the mother wavelet.
The wavelet transform was conducted on a time window, and the result was assumed for the point of the front boundary of the window.
(3) Construct the feature vector of electrodes C3 and C4 for every sampling point, and normalize each feature vector to an interval of [0 1];
(4) Classify each sample point by an adaptive Support Vector Machines (SVM), with a result denoted by St(x) belongs to [-1 1]. 
(5) Accumulate all the previous results (before time point t), a normalized weighted summation, as the classification result of the current time point:

wt is the weight factor determined by a parameter of SVM.

# Text boxes

Select subject-specified scales of complex Morlet wavelet

Use SVM to classify each point and accumulate evidence over time

result

S(t)


Use wavelet to transform the EEG data and construct feature vector

Fig.1.  The procedure from an EEG data to the classification result  

feature