BCI competition 2005: Data set I 
Group information:
Institute of Biomedical Engineering of Xi’an Jiaotong University
Xi’an, 710049, P. R. China
Team Member: Xiaomei Pei, Guangyu Bin 
pei@zy165.com
Supervisor: Prof. Chongxun Zheng. 

Description of our method
Firstly, according to Fisher ratio, the 4 channels with most reactive power features are selected.
Secondly, by EEG signal of 4 channels within 3 sec, 2-order MVAR (multi-variate AR) model is established and the MVAR coefficients are extracted as feature vectors for further classification.
Finally, by Fisher Discriminant Analysis, the two EEG patterns could be discriminated.  
2. Format of the data
The result is saved in a Matlab-file format. res.mat is the classification output with labels -1, 1 of the test data.